## Slide 1: Water Resource Management in Tulkarm Governorate
Prepared By:
Diana Khalid AL-Tayyah
Hala Bilal Takrori

## Slide 2: Objectives
Study the existing water situation for Tulkarm Governorate.
Estimate the Future Water Demand.
Suggest new water resources to cover the water Gap for the next 20 years

## Slide 3: Study Area

## Slide 4: Cont.
The total number of localities is 34
The total population is 163,000

## Slide 6: Study Area
Land use
Topography
Climate
Rainfall rate

## Slide 7: Water situation
The total number of localities is 34
The total number of served localities is 24
The total number of un-served localities is 10
Total existing water supply is around 7.1Mcm/yr.
The average water demand is 126L/C/day

## Slide 8: Future Population
The population growth rates are assumed to be:
3% for years 2007-2010
2.5% for years 2010-2020
2% for years 2020-2030
The total Future population will be around 244,000 by year 2030

## Slide 9: Future Demand
Assumptions:
The water consumption rate will be 100L/c/day.
The increase per year of consumption is 2L/c/day

## Slide 10: Cont.
The existing consumption rate of un-served rural areas is 35L/c/day
The losses in the networks due to leakage, wrong readings in meters and illegal consumption are assumed to decrease.

## Slide 11: clusters

## Slide 12: Existing and Future Population
Cluster Number | Cluster Name | Existing Population ( 2007 ) | Future Population (2030)
1 | Qaffin | 8,546 | 13,504
2 | Baqa | 6,377 | 7,862
3 | An-Nazlat | 2,766 | 4,362
4 | Seida | 9,037 | 14,235
5 | A’ttil | 11,783 | 18,580
6 | Deir Al-Ghusun | 15,895 | 25,065
7 | Tulkarm | 70,445 | 96,084
8 | Anabta | 11,300 | 17,819
9 | Shufa | 5,802 | 9,149
10 | Beit Lid | 7,492 | 11,814
11 | Al-kafreyat | 6,816 | 10,393
Total |  | 156, 259 | 228,866

## Slide 13: Existing Water Supply
Cluster Number | Cluster Name | Existing Supply (m3/year) | Existing Supply (Mcm/year)
1 | Qaffin | 336,070 | 0.336
2 | Baqa | Un-served | Un-served
3 | An-Nazlat | 65,000 | 0.065
4 | Seida | Un-served | Un-served
5 | A’ttil | 595,317 | 0.60
6 | Deir Al-Ghusun | 675,611 | 0.676
7 | Tulkarm | 4,357,278 | 4.357
8 | Anabta | 398,688 | 0.40
9 | Shufa | 202,080 | 0.202
10 | Beit Lid | 217,446 | 0.217
11 | Al-kafreyat | 288,469 | 0.288
Total |  | 7,135,959 | 7.14

## Slide 14: Future Water Demand
Cluster Number | Cluster Name | Future Water Demand (Mcm/year) |  | 
 |  | 2010 | 2020 | 2030
1 | Qaffin | 0.56 | 0.78 | 0.975
2 | Baqa | 0.156 | 0.31 | 0.365
3 | An-Nazlat | 0.152 | 0.23 | 0.28
4 | Seida | 0.35 | 0.69 | 0.81
5 | A’ttil | 0.78 | 1.07 | 1.34
6 | Deir Al-Ghusun | 1.03 | 1.45 | 1.80
7 | Tulkarm | 4.68 | 6.47 | 8.05
8 | Anabta | 0.74 | 1.01 | 1.26
9 | Shufa | 0.36 | 0.50 | 0.614
10 | Beit Lid | 0.47 | 0.67 | 0.826
11 | Al-kafreyat | 0.43 | 0.58 | 0.732
Total |  | 9.708 | 13.76 | 17.052

## Slide 15: Future Water Gap
Cluster Number | Cluster Name | Future Water Gap (Mcm/year) |  | 
 |  | 2010 | 2020 | 2030
1 | Qaffin | 0.224 | 0.444 | 0.639
2 | Baqa | 0.156 | 0.31 | 0.365
3 | An-Nazlat | 0.087 | 0.165 | 0.215
4 | Seida | 0.35 | 0.69 | 0.81
5 | A’ttil | 0.185 | 0.475 | 0.745
6 | Deir Al-Ghusun | 0.354 | 0.774 | 1.124
7 | Tulkarm | 0.323 | 2.11 | 3.69
8 | Anabta | 0.341 | 0.61 | 0.86
9 | Shufa | 0.158 | 0.298 | 0.412
10 | Beit Lid | 0.253 | 0.453 | 0.609
11 | Al-kafreyat | 0.142 | 0.292 | 0.444
Total |  | 2.489 | 6.525 | 9.913

## Slide 16: New and additional water resources
Water Harvesting
Rehabilitation of existing water networks
Water demand management
Ground water wells

## Slide 17: Water Harvesting
Cluster Number | Cluster Name | Existing Population (2007) | Future Population (2030) | Total Number of Buildings | Cistern Volume | 
 |  |  |  |  | (m3/year) | (Mcm/year)
1 | Qaffin | 8,546 | 13,504 | 1,543 | 204,806.98 | 0.205
2 | Baqa | 6,377 | 7,862 | 1,199 | 124,169.546 | 0.124
3 | An-Nzlat | 2,766 | 4,362 | 532 | 70,473.2668 | 0.070
4 | Seida | 9,037 | 14,235 | 1,258 | 166,453.571 | 0.166
5 | A’ttil | 11,783 | 18580 | 2,178 | 288,487.496 | 0.288
6 | Deir Al-Ghusun | 15,895 | 25,065 | 2,929 | 387,976.869 | 0.388
7 | Tulkarm | 70,445 | 96,084 | 9,501 | 1,088,552.82 | 1.089
8 | Anabta | 11,300 | 17,819 | 2,207 | 292,338.829 | 0.292
9 | Shufa | 5,802 | 9,149 | 1,081 | 143,186.108 | 0.143
10 | Beit Lid | 7,492 | 11,814 | 1,472 | 194,978.306 | 0.195
11 | Al-Kafreyat | 6,816 | 10,393 | 1,487 | 190,459.044 | 0.190
Total |  | 156,259 | 228,867 |  | 3,151,882.84 | 3.152

## Slide 18: Rehabilitation of existing water networks
Cluster Number | Cluster Name | Existing water Amounts (m3) | Difference in Losses (%) | Saved Water Amounts | 
 |  |  |  | (m3 / year) | (Mcm/ year)
1 | Qaffin | 336,070 | 10 | 33,607 | 0.034
2 | Baqa | Un-served | 10 | 0 | 0
3 | An-Nzlat | 65,000 | 10 | 6,500.0 | 0.007
4 | Seida | Un served | 10 | 0 | 0
5 | A’ttil | 595,317 | 10 | 59,531.7 | 0.06
6 | Deir Al-Ghusun | 675,611 | 10 | 67,561.1 | 0.068
7 | Tulkarm | 4,357,278 | 10 | 435,727.8 | 0.435
8 | Anabta | 398,688 | 10 | 39,868.8 | 0.04
9 | Shufa | 202,080 | 10 | 20,208 | 0.02
10 | Beit Lid | 217,446 | 10 | 21,744.6 | 0.022
11 | Al-Kafreyat | 288,469 | 10 | 28,846.9 | 0.029
Total |  | 7,135,959 |  | 713,596 | 0.715

## Slide 19: Demand management is the purposeful and beneficial manipulation of the level and timing of water usage

## Slide 20: Ground Water Wells

## Slide 21: Proposed Future Projects
Package # | Description | Total cost ( million $)
1 | A ground water well,2 reservoirs, 2conveyance lines, and one pump | 3.14
2 | A ground water well, one reservoir, one conveyance line and one pump | 2.02
3 | A ground water well,2 reservoirs, 2conveyance lines and one pump | 2.58
4 | A ground water well, one reservoir, one conveyance line and one pump | 1.98
5 | A ground water well, one reservoir, one conveyance line and one pump | 1.98
6 | A ground water well, one reservoir, one conveyance line and one pump | 2.39
7 | A ground water well, one reservoir, one conveyance line and one pump | 2.44
8 | A ground water well, one reservoir, one conveyance line and one pump | 1.98
9 | A ground water well, one reservoir, one conveyance line and one pump | 2.39
10 | A ground water well, one reservoir, one conveyance line and one pump | 1.93

## Slide 22: The total Investment equals 22.83 million $

## Slide 23: Based on the previous packages, the fheaded iollowing cash flow shows the nvestment to implement the plan
Chart: Cash Flow
| 2011 | 2012 | 2013 | 2014 | 2015 | 2016 | 2017 | 2018 | 2019 | 2020 | 2021 | 2022 | 2023 | 2024 | 2025 | 2026 | 2027 | 2028 | 2029 | 2030
 | 2.0933 | 1.0467 | 1.01 | 1.01 | 1.72 | 0.86 | 0.99 | 0.99 | 0.99 | 0.99 | 1.195 | 1.195 | 1.22 | 1.22 | 0.99 | 0.99 | 1.195 | 1.195 | 0.965 | 0.965

## Slide 24
Based on the packages above we can conclude the following:
The total investment cost is considered to be around 22.83 million $ which approximately equals 90 million NIS.
The average investment per year equals around 1,000,000 $/year.
The average investment per capita per year equals around 4.1 $/capita /year.
Maintenance cost per capita equals around 7.4 NIS.

## Slide 25: Thank you for your Listening