## Slide 2
An – Najah National University
Faculty of Engineering
Civil Engineering Department
Pavement Design For Bizzarya – Deir Sharaf highway
Prepared by: Akram Awwad
Zafer hasson
Supervisor : Dr. Sami Hijjawi
2012

## Slide 3
Project description,
Highway problems,
Soil properties,
Traffic data,
Traffic analysis,
Flexible pavement layers,
Rigid pavement design,
Rigid pavement execution,
Slope stability problem, And
Budget evaluation.
Project outline:

## Slide 4
Project description

## Slide 6
Deir – Sharaf intersection
Bizzarya inter section at the end of the highway

## Slide 7
Highway Problems
Cracks in pavement
Drainage
Slope stability
Geometric problems
Others…

## Slide 8
Alligator Cracking
Longitudinal cracking
Transverse crack
Edge crack
Pavement cracks

## Slide 9
Unstable cut area
Slope stability – Burqa village
Slope stability problems

## Slide 10
Closed ditch
Closed culvert
Drainage problems

## Slide 11
Geometric problems

## Slide 12
Damaged barrier

## Slide 13
Soil description
Station | Soil description
0+000 | Soft formation of grayish marlstone
0+150 | Soft formation of grayish marlstone
0+450 | Selected fill materials
0+800 | Light brown silty clay with little boulders and organic matters
1+250 | Yellowish brown silty clay
1+800 | Yellowish formation of soft marlstone
2+100 | Yellowish formation of soft marlstone
2+450 | Soft formation of yellowish marlstone
2+720 | Soft formation of yellowish marlstone
3+320 | Light brown silty clay with little bounders and organic matters
3+650 | Light brown silty clay with little bounders and organic matters
4+100 | Light brown silty clay with little bounders and organic matters
4+350 | Light brown silty clay
4+650 | Yellowish formation of soft marlstone
5+100 | White formation of medium hard marlstone
5+510 | Light brown silty clay mixed with very hard chert
6+500 | Light brown silty clay with little bounders and organic matters
7+000 | Light brown silty clay with little bounders and organic matters
7+500 | Light brown silty clay with little bounders and organic matters
8+000 | Light brown silty clay with little bounders and organic matters
8+200 | Light brown silty clay with very little boulders

## Slide 14
Traffic data
24 – hours count , An – najah national university , 2000
Not used in calculations.
12 – hours count, First Option Company, Ramallah, Palestine
26/8/2008, 12 – Hours counting:
Peak hour (15:00 – 16:00)
Peak hour volume (PHV) = 242 Veh.
27/8/2008, 12 – Hours counting:
Peak hour (8:00 – 9:00)
Peak hour volume (PHV) = 265 Veh.
4 – Hours counting (7:00am-9:00am & 3:00pm-5:00pm) performed in Wednesday 16/3/2011 on Bizzarya – Deir Sharaf road for two directions counted every 15 min. this counting obtained by (Ring Road Graduation project 2011, students; Mohammad Assrawi, Odai Salahat, Nidal Abu Aisheh)

## Slide 15
Traffic analysis
Percent of 4 – hours count to 12 – hours = 37%
Percent of 12 – day hours to the 24 - hours traffic = 85%
Percent of 4 – hours to 24 – hours traffic = 0.37 * 0.85 = 30%
Expansion factor = (total day traffic / particular hour traffic) = 1/0.30 = 3.3
Chart: 
| PC | Bus | Mini Bus | Truck | Trailer
 | 977 | 17 | 62 | 77 | 6

## Slide 16
Pavement design

## Slide 17
Segment | Station (m) |  | Segment length (m) | CBR %
 | From | To |  | 
1 | 0+000 | 1+250 | 1,250 | 8
2 | 1+250 | 4+650 | 3,400 | 6
3 | 4+650 | 5+100 | 450 | 45
4 | 5+100 | 8+200 | 3,100 | 3
Segments for design…

## Slide 18
Segment | Sub – Grade CBR | Station (m) |  | Depths (cm) |  | 
 |  | From | To | Asphalt | Base course | Sub - base
1 | 8 | 0+000 | 1+250 | 7 | 20 | 15
2 | 6 | 1+250 | 4+650 | 7 | 20 | 15
3 | 45 | 4+650 | 5+100 | 7 | 30 | ----
4 | 3 | 5+100 | 8+200 | 7 | 25 | 30
Flexible pavement layers

## Slide 19
Thicknesses |  |  |  |  | 
Segment | Sub – Grade CBR | Station (m) |  | Depths (cm) | 
 |  | From | To | Concrete | Sub - base
1 | 8 | 0+000 | 1+250 | 15 | 25
2 | 6 | 1+250 | 4+650 | 15 | 30
3 | 45 | 4+650 | 5+100 | 15 | 15
4 | 3 | 5+100 | 8+200 | 15 | 30
Reinforcement |  |  | 
Segment | Steel location | Diameter and spacing | Number of bars/piece
All segments | Long. Temperature steel | 1ф8 /15 cm | 24
 | Trans. Temperature steel | 1ф8 /30 cm | 40
 | Dowel Bars | 1ф32 / 30 cm | 12
 | Tying Bars | 1ф20 / 90 cm | 14
Rigid pavement design

## Slide 20
Reinforcement distribution

## Slide 21
Expansion joint design
Contraction joint design
Hinge joint design
Joints design

## Slide 22
Dowel bars
Shrinkage steel
Tying bars
Rigid pavement execution

## Slide 23
Concrete placement

## Slide 24
Vibrating

## Slide 25
Finishing and sawing

## Slide 26
Concrete and joints sealing

## Slide 27
Slope stability

## Slide 28
Burqa intersection located In segment 4 at stations (from 5+100 to 8+200) and the type of soil as the following table
No. | Station (m) | Depth (m) |  | Description | W (%) | Finer sieve #200 (%) | PI | MDD (g/cm3) | O.M.C (%) | CBR (%)
 |  | From | To |  |  |  |  |  |  | 
14 | 5+100 | 0.25 | 1.60 | White formation of medium hard marlstone | 8.5 | 17.0 | 2.50 | 1.810 | 7.4 | 45
15 | 5+510 | 0.25 | 2.00 | Light brown silty clay mixed with very hard chert | 9.4 | 27.3 | 26.50 | 1.937 | 7.4 | 10
16 | 6+500 | 0.25 | 2.00 | Light brown silty clay with little boulders and organic matters | 14.3 | 46.0 | 12.50 | 1.900 | 14.2 | 15
17 | 7+000 | 0.25 | 2.00 | Light brown silty clay with little boulders and organic matters | 14.5 | 78.0 | 12.50 | 1.642 | 15.5 | 3
18 | 7+500 | 0.25 | 2.00 | Light brown silty clay with little boulders and organic matters | 14 | 81.0 | 12.70 | 1.638 | 15.0 | 3
19 | 8+000 | 0.25 | 2.00 | Light brown silty clay with little boulders and organic matters | 14.3 | 80.0 | 12.20 | 1.645 | 15.3 | 3
20 | 8+200 | 0.37 | 2.00 | Light brown silty clay with very little boulders | 22 | 90.0 | 22.00 | 1.635 | 23.5 | 2

## Slide 30
Factor of safety = 1.67 > 1.5 … OK

## Slide 31
In general , the lands beside the Burqa intersection is agricultural , so the soil is weak and can be absorbed the water in winter season ,then it will collapse. So the lab. Test (Tri – axial unconfined test ) gives the following data:
Cohesive (c in KN/m2) | Phi ( in degrees) | Unit weight (ɣ in KN/m3)
35 | 8 | 18
And the load traffic = 20 KN/m2

## Slide 32
Budget evaluation

## Slide 33
Rigid pavement cost estimation |  |  |  | 
Material type | Quantity | unit | Unit cost (NIS) | Cost (NIS)
Concrete | 8856 | M3 | 320 | 2,833,920
Sub – base coarse | 17708 | M3 | 30 | 531,240
Steel φ 32 | 103.689 | Ton | 3500 | 362,912
Steel φ 20 | 23.627 | Ton | 3500 | 82,695
Steel φ 8 | 233.301 | Ton | 3500 | 816,554
Base coarse | 656 | M3 | 50 | 32,800
Total cost (NIS) |  |  |  | 4,660,121
Flexible pavement cost estimation |  |  |  | 
Cost (NIS) | Unit cost (NIS) | Unit | Quantity | Material type
3,306,400 | 800 | M3 | 4133 | Asphalt
722,650 | 50 | M3 | 14453 | Base course
390,600 | 30 | M3 | 13020 | Sub – base coarse
4,419,650 | Total cost (NIS) |  |  | 

## Slide 34
Conclusion:
Flexible pavement is cheaper than rigid pavement, also rigid pavement execution needs high initial investment cost, however it can last for 50 years compared with 25 years in flexible.
Slope stability near Burqa is a critical case because safety factor equals 1.671 and its close to the critical value of 1.5, so suitable solution should be prepared in future such as soil nailing or boulders above rock layers.

## Slide 35
Thank you for your attention