## Slide 1
Design of Bala School
JAFAR NATOUR
JAD SULAIMAN
DR.RIYAD ABD-ALKARIM
PREPARED BY :
SUPERVISOR:

## Slide 2: the project consist of five chapter. 1- chapter one : general introduction 2- chapter two: design of floor system 3-chapter three : beams design 4-chapter four : column design 5-chapter five : footing design
PROJECT DESCRIPTION

## Slide 3
Typical column and wall layout

## Slide 4
General view of the project

## Slide 5: Chapter One: General Introduction
  About the project
  Philosophy of analysis & design codes
  Materials
  Loads
  Codes

## Slide 6: Introduction
About The Project:
The school is located in the "Bala" town in “Tulkarem” district , the school consists of two parts. The first part consists of three floors with 3.25 m per floor and a plan area of 488.5 m2 . The second part consists one floor with an area of 275m2 separated from the first part by a structural break.

## Slide 7: Introduction
Philosophy Of Analysis & Design Codes
  The method used in design is the “Ultimate Design Method” .
  The codes used:
          The American Concrete Institute (ACI) code 2008 .
          The International Building Code (IBC-2009).
  The analyzing program is SAP 2000 v15.1

## Slide 8: Introduction
Material
  Concrete strength for footing 30 Mpa.
  Concrete strength for column 28 Mpa.
  Concrete strength for other element 24 Mpa.

## Slide 9: Introduction
Loads :
  Live load for class = 2KN/m2
  Live load for corridor = 4KN/m2
  S.I.D.L = 4 KN/m2.
Load Combination :
  1.4D
  1.2D+1.6 L

## Slide 10: Chapter Two Design Of Floor System
  Structural system of the slab
  Slab thickness
  Design of rib slab

## Slide 11: Slabs design
Structural System Of The Slab:
  The structural system used is one way ribbed slab.
Slab Thickness:
  L/18.5 =270/18.5 =14.5cm (a thickness of 20 cm is considered).
Typical section in the ribbed slab

## Slide 12: Slab design
Rib distribution of the right part of the school

## Slide 13: Slab design
Rib distribution of the left part of the school

## Slide 14: Slab design
maximum negative moment = 12.4 for rib
= 6.45
→
Use (2Ø 10 mm).
Design Of Slab For Flexure:

## Slide 15: Slab design
Design of slab for shear
  =
  Use stirrups Φ 8mm/250mm (just to place the bars)

## Slide 16: Chapter Three: Beams Design
  Selection of beams section.
  Design for moment.
  Design for shear.
  Design for torsion.

## Slide 17: Beams Design
Selection of beams section based on deflection requirement:
The minimum thickness of the beam Use thickness of 50 cm

## Slide 18: Beams Design
Selection of beams sections based on capacity of the bending moment:
  .
  For simply supported beam,
  Assuming that
  .

## Slide 19: Beams Design
Design of beams for flexure
  Beams design based on the value of the &(moment that subjected to it
A value of (¼) of the longitudinal torsion reinforcing is add for each bottom and top steel for the beams that subjected to torsional forces

## Slide 20: Beams Design
General note about beams reinforcing
  The top and bottom bar shall be splices at the beam supports for the splice length identified in ACI code.
  The top and bottom bar shall be extend an anchorage length of 50 from the face of the external supports.

## Slide 21: Beams Design
Design of beams for shear:

## Slide 22: Beams Design
For beams subjected to shear only:
  .
where: : the area of steel that resist shear
s : spacing between stirrups &

## Slide 23: Beams Design
Design Of Beams For Torsion
  Torsion reinforcement shall consist of longitudinal and traverse reinforcing.
  the longitudinal reinforcing distribute on the bottom and top reinforcing of the beams with a percent of (1/4) of torsional reinforcement and (1/2) on the middle of the beam.
  Torsional travers reinforcement is add to the shear reinforcement as

## Slide 24: Chapter Four: Columns Design
Selection of columns cross section.
Check the slenderness of columns.
Column interaction diagram .
Column grouping .

## Slide 25: Columns Design
Selection of column cross section:
  For the maximum ultimate columns load a check of the area gross is made
  The maximum ultimate load = 870 KN
  Assuming value is minimum = .01 for column
  Where , the above equation can be approximated to
  A section of 50*25 cm is used.

## Slide 26: Columns Design
Check The Slenderness Of The Columns
Where: = unsupported length of member
= radius of gyration = .3 for rectangle cross section
For non -sway frame , any column taken , with K conservatively taken 1, and then then the column is consider to be short column

## Slide 27: Columns Design
Column interaction diagram:
  Assuming the minimum value of for the column reinforcement whichis equal .01 and check it in the sap, the interaction diagram then obtain .
Chart: column with max load
| 0 | 71.979600000000005 | 111.91470000000002 | 142.83200000000062 | 164.16409999999999 | 178.35280000000066 | 195.05940000000001 | 201.01569999999998 | 154.15780000000001 | 71.742400000000004 | 0
interaction diagram | -1805.766 | -1805.766 | -1667 | -1405.71 | -1127.473 | -818.7222 | -750.283 | -620.0444 | -312.435 | 138.1145 | 474.768
point of load and moment | -867.5
Chart: column with maximum moment
| 0 | 71.979600000000005 | 111.91470000000002 | 142.83200000000062 | 164.16409999999999 | 178.35280000000066 | 195.05940000000001 | 201.01569999999998 | 154.15780000000001 | 71.742400000000004 | 0
interaction diagram | -1805.766 | -1805.766 | -1667 | -1405.71 | -1127.473 | -818.7222 | -750.283 | -620.0444 | -312.435 | 138.1145 | 474.768
point of load and moment | -172

## Slide 28: Columns Design
Column Grouping:
Column is classified based on ultimate loads and based on reinforcement.
  Based on load
    Columns is classified from c1 to c9
  Based on reinforcing
    Columns is classified from c1 to c3
  An illustrator drawings in the next two slides

## Slide 29: Columns Design

## Slide 30: Columns Design

## Slide 31: chapter Five: Footings Design
  Selection of footings type .
  Distribution of footings on the columns and shear wall.
  Distribution of the tie beams

## Slide 32: Footing Design
The footing type used is four types
  Single footings.
    Used for the most of the columns where either near columns footings nor structural break
  Companied footings
    Used for the columns footings which is closely to each other and no enough space for single footings for each columns
  Strap footings.
    Used for the column lies on the structural break
  Wall footings.
    Used for the wall

## Slide 33: Footing Design