## Slide 1: Preberd by: Azza Yahya Israa Labadi Nedaa Bouzia Raghad Melhem
Submitted to:
Dr.Sami Hijawi
Foundation Construction On Expansive Soil And Methods Of Improvement
2013

## Slide 2
content
introduction
Loads in columns
Mat design
Pile design
cost analysis
conclusion

## Slide 3
BUILDING PLAN

## Slide 4
Loads in column
column number | column dimensions(cm) | DL (KN) | LL (KN) | Service load (KN) | ultimate load (KN)
c1 | R=25 | 511.85 | 54.18 | 566.03 | 700.91
c2 | 90*20 | 1011.81 | 330.96 | 1342.77 | 1743.71
c3 | 90*20 | 678.17 | 207.69 | 885.86 | 1146.10
c4 | 150*20 | 853.65 | 283.50 | 1137.15 | 1477.98
c5 | 80*20 | 869.37 | 162.75 | 1032.12 | 1303.64
c6 | 90*30 | 424.10 | 133.14 | 557.24 | 721.95
c7 | 60*25 | 576.79 | 172.62 | 749.41 | 968.34
c8 | 80*20 | 555.66 | 340.20 | 895.86 | 1211.11
c9 | 150*20 | 621.17 | 380.31 | 1001.48 | 1353.90
c10 | 80*20 | 560.46 | 343.14 | 903.60 | 1221.58
c11 | 80*20 | 451.43 | 149.10 | 600.53 | 780.28
c12 | 80*20 | 386.23 | 156.24 | 542.47 | 713.46
c13 | 80*20 | 455.85 | 279.09 | 734.94 | 993.56
c14 | 80*20 | 540.23 | 330.75 | 870.98 | 1177.47
c15 | 80*20 | 514.50 | 315.00 | 829.50 | 1121.40
c16 | 80*20 | 429.09 | 151.62 | 580.71 | 757.50
c17 | 80*20 | 387.63 | 147.84 | 535.47 | 701.70

## Slide 5
Centroid location

## Slide 6
Thickness:
For column # 11
PU = 780 KN
d = 15((Pu) ^1/2) = 420.
VU = PU = 780 KN
ϕVc = (0.75 *(1/3) * √28*(1700 + 2d) * 460 / 1000
ϕVc = VU => d = 420 mm, h = 500 mm
Thickness

## Slide 7
Mat Design
SAP design:
-Assume:
* F’c= 28 MPa
* Fy= 420 MPa.
-Soil bearing capacity qsoil=
200 KN/m2.
-Weight per unit volume=
25 KN/m3.
-Modulus of Elasticity, E=
4700
Information needed:

## Slide 8: Results:
The maximum deflection was 6.3 mm which less than the allowable deflection 10 mm => ok
Deflection:
Mat Design

## Slide 9
Moment:
Designed strip location
Mat Design

## Slide 10
M | AS | p | Ø18 - Number of bars
228.75 | 1058.68 | 0.001825 | 5
105.4 | 483.5028 | 0.000834 | 2
Asmin= 0.0018*b*h
p =
As= p*b*d.
Reinforcement:
Mat Design

## Slide 11: Determination of allowable pile capacity : Qulti =Qs+Qp Qs : frictional resistance = ∑∆Lρfavg Qp: Load carrying capacity of the pile point = 9CuAp Qall = Qulti/F.S = 399.5 KN , Where F.S = 3 here No. of needed piles= service load/ Qall Estimate of pile cap dimensions L g = (n1-1)d + 2(D\2) Bg = (n2-1)d + 2(D\2) The following table shows the relation between(L,D) and the corresponding values of allowable bearing capacity .
Pile design

## Slide 12
L (m) D(m) | 6m | 8m | 10m | 12m | 14m | 16m | 18m
0.5m | 217.7 | 292.9 | 360 | 445.8 | 529 | 616.7 | 712.5
0.6m | 267.6 | 357.8 | 438.4 | 541.4 | 641.2 | 746.4 | 861.3
0.7m | 319.65 | 424.9 | 518.9 | 639 | 755.5 | 878.2 | 1012
0.8m | 373.8 | 494.1 | 601.5 | 738.8 | 871.9 | 1012 | 1165
0.9m | 430 | 565.4 | 686.2 | 840.7 | 990.4 | 1148 | 1321
1.0m | 488. | 638.8 | 773.1 | 944.7 | 1111 | 1286 | 1478
Cap dimensions | No. of piles | Pile size (L,D) | Service Load(KN) | Foundation No. | Column No.
29 caps | 53 piles |  |  |  | 
0.8 , 0,8 | single | 10 , 0.8 | 345.94 | F1 | S3
0.8 , 0,8 | single | 10 , 0.8 | 566 | F2 | C1,C6,C12,C17
0.8 , 0,8 | single | 10 , 0.8 | 620 | F3 | C11,C16,C20
2.8 ,0.8 | 2 | 8 , 0.8 | 749.4 | F4 | C7,C13,C21
2.8 ,0.8 | 2 | 8 , 0.8 | 903.6 | F5 | S1,C3,C8,C10,C14,C15,C26
2.8 ,0.8 | 2 | 10 , 0.8 | 1139.18 | F6 | C4,C5,C9,C18,C22,C23
2.8 ,0.8 | 2 | 12, 0.8 | 1410.15 | F7 | S2,C2,C19,C24
2.8,2.8 | 3 | 10 , 0.8 | 1707.8 | F8 | C25
2.8 , 2.8 | 4 | 12 ,0.8 | 2502 | F9 | S4
Pile design

## Slide 13
The structural design of the pile depends on the nature of the soil
Asmin = 0.005Ag=0.005(5026.5)=25.13 cm² (10ф18 mm)
Spacing of ties = (1ϕ8/250) .
Design of pile cap :
Vu = ϕVc ( to calculate the thickness )
The As then computed for the cap with ρ=0.002 .
The efficiency of the group of piles are calculated and these should be >1 to be in the safe side .
Efficency =
Pile design

## Slide 14: Mat Foundation Cost Analysis:
Cost Analysis
Excavation cost:
Total volume of excavated soil = 565.9 CM
Cost/hr= 400 NIS
The productivity of excavator=100 CM/hr.
Duration = (quantity / (productivity* no. or resources))
Duration = 565.9 / (100*1)=5.7hrs use 6hrs.
>>Cost= 6*400 =2,400NIS.
Backfilling cost:
Backfill and Base coarse
>>Cost= 10,986NIS.

## Slide 15
Cost Analysis
Steel :
Steel (kg) = , φ = 18
Total Steel weight = 14,275 kg >>> 14.27 Ton
>>>Cost = 14274.9*3.2NIS/Kg =45,679 NIS
Concrete :
Total volume of concrete = 229.88 CM
Concrete cost = 229.88*320NIS/CM=73,562NIS
Total cost = (concrete +steel +excavation & backfilling) = 132,628NIS
Indirect cost=(Tax+Profit+overhead)%=0.3xCost=0.3*132627=39,788NIS
>>>Price = 132,628+39,788=172,416 NIS

## Slide 16
Cost Analysis
Pile Foundation Cost Analysis:
Concrete:
Volume, pile =xNo.of piles =5x53=266 CM
Volume ,Cap=L.W.DxNo.= 1.6x1.6x.85x29= 63 CM
>>>Cost= (266.4+63.1)x320=105,440 NIS.
Steel :-
**(As,pile + Stirrups,pile)xNo. =(218+32.2)x53= 250x53=13,264 kg
**Pile Cap (Kg) = 54x27=1,458 kg.
>>Cost = (1458+13264.3) X3.2NIS/Kg= 47,111 NIS.

## Slide 17
Cost Analysis
Drilling cost:-
Drilling&processing=250NIS/CM+120NIS/pile
=250x330+120x53=82375+6360=88,735NIS
Cost= (concrete+steel+drilling &processing)=105440+47111+88735=241,286NIS
Indirect Cost =(Tax + Profit +overhead)%=30%xCost=30%x241286=72,386NIS
>>>Price = 241286 +72386=313,672NIS

## Slide 18
Pile Price = 313,672NIS >> *Mat Price = 172,416 NIS
As the price of mat foundation is less than the price of the pile then, the mat foundation is recommend to use in this case. In the other hand, mat (Raft) foundation is easier in construction in most of its activities.
Conclusion:

## Slide 19
Thank You