## Slide 1: بسم الله الرحمن الرحيم

## Slide 2: Foundation design for Al Ashqar center
An-Najah National University
Faculty of Engineering
Civil Engineering Department
Prepared by:
Eslam Horani
Zaid Saidi
Supervisor:
Dr.Sami Hijjawi.

## Slide 3: The Project
The site is located in Tulkarem city.
The building consists of seven stories, and the area of each stories is about 700 m2 , the aim of this research is to design foundations that are practical and economic.

## Slide 4: Project continue ………..

## Slide 5: This project contains :
Chapter one: Introduction.
Chapter two: literature view .
Chapter three: site investigation and soil report.
Chapter four: Geotechnical and structural design of foundation.
Appendix and references.

## Slide 6: Types of Foundations:
Shallow foundations:
Shallow foundations are those founded near to the finished ground surface, generally where the founding depth (Df) is less than 3 m.
Types of shallow foundations:
1. Isolated footing.

## Slide 7: Shallow foundations types
2.Combined footings.

## Slide 8: Shallow foundations types
3.Continuous footings.
4.Strap footing.

## Slide 9: Shallow foundations types
5.Mat foundation.

## Slide 10: Structural system
As we know any structure consist from elements ,these elements can be classified into:
Slab.
Columns.
Beams.
Walls.
Foundation.

## Slide 11: loads
Load calculations:
The load calculations in this project was calculated by Sap program.
Live load = 400 Kg/ m2
super imposed dead load = 500Kg/m²

## Slide 12: structural analysis using sap 2000
In this project we use sap 2000 to analyze the load and find the reaction at all columns .
The reaction of footings from column :

## Slide 13: Table 1 : The reaction of footings

## Slide 14: Site Investigation
The Site Investigation of the site were studied through comprehensive site investigation, carried out on January 2011 by Hijjawi Engineering laboratories.
Five boreholes were dug out in site to carry the subsurface investigation.

## Slide 15: Site Description
The geological report shows that the site consists mostly of moist and plastic formations of soft creamy marlstone within the whole depth of exploration and covered by a thin layer of silty clay .
The collected sample was tested for physical and mechanical properties .the following are the main soil properties required for foundation design purposes.

## Slide 16: Calculating of baring capacity of soil
Cohesion ( c ) = 20 kN/m2
Angle of internal friction (Ø) = 13
Unit weight (γ) = 16 kN/m3
According to bearing capacity equations, the allowable bearing capacity is 2.2 kg/cm2.

## Slide 17: Geotechnical and structural design of foundation
After analysis of the structure and loads of columns, geotechnical and structural design.
The first trial is to try to design single footing by manual calculations.
The second trial is to try to design single footing by using RCD program to area of single footing
The third trial is to design mat foundation by using SAP program

## Slide 18: Design of single footing
Determine the loads
Calculate area of footing
Check for wide beam shear
Check for punching shear

## Slide 19
Find the value of
Design for Flexural reinforcement
Calculate area of steel
Check
Check

## Slide 20
Isolated footings
Bearing capacity of the soil is 2.2 kg/cm2
Group name | Area of footing (m2) | Thickness (cm) | Bar used/m*
F1 | 2.0x2.2 | 35 | 8Φ16
F2 | 2.1x2.3 | 35 | 10Φ16
F3 | 1.3x1.5 | 35 | 5Φ16
F4 | 1.6x1.8 | 35 | 5Φ16
F5 | 2.1x2.1 | 40 | 10Φ16
F6 | 2.0x2.0 | 40 | 8Φ16
F7 | 1.5x1.5 | 35 | 5Φ16

## Slide 21: Settlemnt
The allowable settlement in isolated footing
is 25 mm and the allowable differential settlement is 19
The settlement calculations for all footings are less than the allowable , the design is ok

## Slide 22: Design Mat Foundation
A second foundation choice for the suggested building project is mat foundation .
Our proposed structure is symmetry and we use the SAP program for taking the moment .

## Slide 23: The picture below takes from SAP shows the mat foundation .

## Slide 24: steps for designing the mat foundation
check punching shear for finding the depth of mat :
Applying the equation of punching shear on the critical column with load equal 150 ton.

## Slide 25: steps for designing the mat foundation
Ultimate load =150 ton
h=70cm
cover = 7 cm
Assume d=63cm
Use qu = qall =22ton/m2
Vu=150– (30*0.63) =131 ton
Φ *Vc = Φ /6 (1+(2/βc)√f'c*bo*d
bo=1051 mm
0.75/6(1+(2/(50/30)) √24*2102*630/1000=1784 kN=182 ton

## Slide 26: Continue …..
Φ*Vc = Φ (0.33)√f'c*bo*d
=0.75*0.33* √24*2102*630/1000 =1606KN=164 ton
OK
Use
h=70cm
d=63cm

## Slide 27: steps for designing the mat foundation
2. The parameter used were :
Mat depth = 0.70 m .
Fc = 240 kg / cm2
fy = 4200 kg / cm2

## Slide 28: steps for designing the mat foundation
3. calculate steel ratio (𝜌 ) :
From SAP we find the ultimate moment on x- direction and on y-direction .
we find the maximum positive moment and the maximum negative moment.
After finding Mu we apply the equation of steel ratio (𝜌 ) then finding area of steel then number of bars .

## Slide 29: steps for designing the mat foundation
AST = 𝜌 . b . d where ( b , d ) in cm .
𝜌min = 0.0018 .
ASTmin = 0.0018 * b * h .
Take the maximum positive moment and the maximum negative moment and then find the area of steel ( take the larger area of steel between the AST from moment and the ASTmin ).

## Slide 30: Result of analysis of the mat foundation
The output data and their calculations in details are according to strips and middle strips in both direction x and y axis .
M11 due to x-axis and M22 due to y-axis .
The distributing of steel bars in mat must be in correct way so as to help labors in the site of the work .
The reinforcement depends upon the sign of moment . The negative moment take the top steel and the positive moment take the bottom steel bars .

## Slide 31: Moment in x direction ( M11 ) :

## Slide 32: reinforcement in X-direction
Notes | Top steel | Bottom steel | Section
Bottom steel required under columns & between columns. | 10Φ20/m | 10Φ20/m | 1
 | 8 Φ20/m | Use 5 Φ18/m | 2
 | 7Φ20/m | 5 Φ20/m | 3
 | 7Φ20/m | 4 Φ20/m | 4
 | 7Φ20/m | 4 Φ20/m | 5
Top steel can be reduced as span length reduce as appear in BM diagram | 10Φ20/m | 10Φ20/m | 6

## Slide 33: Moment in Y direction ( M22 ) :

## Slide 34: reinforcement in Y-direction
Notes | Top steel | Bottom Steel | Section
Bottom steel required under columns (except column 19) & between columns. | 4 Φ20/m | 5 Φ20/m | 1
 | 4 Φ20/m | 5 Φ20/m | 2
 | 4 Φ20/m | 5 Φ20/m | 3
Top steel can be reduced as span length reduce as appear in BM diagram | 4 Φ20/m | 5 Φ20/m | 4
 | 4 Φ20/m | 5 Φ20/m | 5
 | 4 Φ20/m | 5 Φ20/m | 9

## Slide 35: Settlemnt
The allowable settlement in mat footing
is 50mm and the allowable differential settlement is 19 mm
The settlement calculations for all footings are less than the allowable , the design is ok

## Slide 36: Thanks for listening